## Slide 1
PROJECT
AUR FINAL

## Slide 2
CONTENT
01
02
03
04
OUR TEAM
MECHANICAL
HARDWARE
SOFTWARE
4.1 CONSOLE
4.2 EMBEDDED
4.3 MOTION & LOCALIZATION

## Slide 3
OUR TEAM
Mechanical:
Hardware:
Software:
Habiba Abdel Hameed
Ahmed El-Masry
Ahmed Sameh
Ahmad Hossam
Youssef Samy
Amr Sokkar
Mohammed Nabil
Aly Mohie

## Slide 4
Mechanical
Materials & Dimensions:
Chassis Material: Wood
Advantages:
  Light
  Easier to Shape
  Budget-Friendly
  Perfect for quick modifications
  Laser-cut to precise dimensions of 400*226mm
  Motors: DC Motor GA25-370
  Mass: 6 kg
  Incline: θ = 0 (flat playground)
  Acceleration: 0.5 m/s²
  Efficiency:70%
  Output Torque: ≈ 0.9 kg.cm
  RPM: 100
  Why GA25-370?
  High torque for effective acceleration
  Ideal for small spaces
  Prioritizing acceleration over top speed
  Equipped with encoders for precise localization
  Servo Selection:
  MG945: 10.5 kg.cm torque  for raising and lowering the arm)
  SG5010: 5.5 kg.cm torque  for opening and closing the gripper
  Wheels:
  Robot Wheel 65mm  high grip rubber

## Slide 5
Electrical
L293D Motor Driver IC :
  Why Use L293D?
  Built-in durability and protection make it a robust choice for motor control!
  Key Features:
  Dual H-bridge: Controls two motors independently
  Operating Voltage: Logic voltage of 4.5V to 7V (Vcc1); motor voltage up to 36V (Vcc2)
  Current Handling: Up to 600mA continuous current per channel (1.2A peak)
  Thermal Shutdown: Prevents overheating
  Internal Protection Diodes: Safeguards against back-EMF from motors
  Bidirectional Control: Enables forward and reverse motion
  Enable Pins: Manage motor states (enabled/disabled)

## Slide 6
Software
4.1 Console:
UI Components:
  Video Feed Display: Shows live footage, with buttons to select different vision algorithms.
  Dynamic Box List: Lists all detected boxes and their coordinates in real time.
  Dynamic Map: Continuously updates with the robot's current position.
Navigation & Control System:
  We use the Gamepad API, standard in all major web browsers, to process gamepad inputs with a game-loop-like algorithm polling every 15 ms.
  Key Features:
Input Precedence: The algorithm prioritizes inputs to prevent wheel differential damage.
Forward/Backward Motion: Calculated by subtracting the L2 value from the R2 value
Right Analog Stick Calibration: Before use, a full rotation calibrates the stick via the controller's firmware, with an error margin of 0.1 accounted for in any direction. Vertical directions and irrelevant inputs are ignored.

## Slide 7
Software
4.1 Console:
Computer Vision:
  Detects and decodes QR codes on every box
  Assigns a unique box number to each code
  Assists the navigator in tracking and managing box destinations efficiently
The Algorithms made available:
Library | Strength | Weakness
pyzbar | Extremely Efficient | Angled Codes
Cv2- builtin | Angled Codes | Less Efficient
qreader | Deepest Detection | Least Efficient
Communication:
Host | Component | Connects to
Mobile | IMU | Console w/ HTTP GET
Mobile | Camera | Console w/ HTTP
Console | MQTT Broker | ESP-32WR00M
Console-Backend | Flask & Socket IO | Frontend

## Slide 8
Software
4.2 Embedded:
Goals for ESP-32WROOM Programming:
  Receive motion commands from the console and translate them for motor control
  Convert arm and gripper commands into servo-friendly instructions
  Send encoder data to the console for localization
  Use RTOS to separate receiving, sending, and callbacks into different tasks

## Slide 9
Software
4.3 Motion & Localization:
Console and Motion Goals:
  Get Gamepad commands from console
  Map values from 0 → 1 to 0 → 255
  Prepare values for differential steering
  (e.g., for right rotation at speed x,  add x speed to the right wheel and -x speed to the left wheel)
  Receive encoder readings from the ESP-32WROOM and IMU data from the mobile phone
  Apply a Kalman filter for accurate localization

## Slide 10
Software
4.3 Motion & Localization:
Goals for Localization:
  Receive data from Wheel Encoders & Receive IMU data from Mobile Phone’s Sensors
  Apply Extended Kalman Filter to get more accurate coordinates for Robot’s Position
Extended Kalman Filter:
  1. Initialization Phase:
  The FusionEKF class is created to manage state estimation using an Extended Kalman Filter (EKF).
  When process_measurement is called for the first time ,The state vector self.ekf_.x is initialized to zeros, representing [px, py, vx, vy, yaw, yaw_rate].
  The previous_timestamp is set to the current timestamp.
  The is_initialized flag is set to True to prevent reinitialization.

## Slide 11
Software
4.3 Motion & Localization:
Extended Kalman Filter:
2. Prediction Step:
For Subsequent sensor data:
  The time difference dt between the current and previous timestamps is calculated
  The State Transition matrix F is updated to incorporate the time effect on position
  The EKF predicts the next state using this updated matrix and a process noise covariance
  3.Measurement Update:
The filter updates the state using measurements from different sensors
IMU Measurements:
  Accelerometer and gyroscope data update the state for yaw and velocity
Wheel Encoder Measurements:
  Distance data from left and right encoders calculate changes in position
  The EKF updates the state vector with these values.